## Slide 1: Fully Distributed Joint Localization and Target Tracking With Mobile Robot Networks

## Slide 2: Problem Statement
The study addresses the challenge of enabling a team of mobile robots with onboard sensors to simultaneously localize themselves and track multiple targets.
A fully distributed algorithm is introduced, which is robust to various dynamics such as time-varying sensing, communication topologies, and changing blind robots (robots not directly sensing the targets).
Each robot can estimate the pose (position and orientation) of itself (localization) and the states of targets (tracking) using only its local information and information from its one-hop communicating neighbors while preserving consistency

## Slide 3: Other solutions
Centralized-Equivalent Algorithms: These are not fully distributed and require some variables to be shared among the team through information propagation rather than one-hop neighbor-to-neighbor communication.
Extended Kalman Filter (EKF)-Based Approaches: These include asynchronous communication handling and approximation of cross correlations between robots, but may lead to inconsistent estimates.
Covariance Intersection (CI) Technique: Used to compute a consistent estimate, but requires a specific measurement model and is limited to relative poses of neighbors34.
Interleaved Update (IU) Algorithm: Handles generic models and computes consistent estimates, but requires maintaining multiple filters and tracking the origin of measurements.

## Slide 4: Proposed Solution
Distributed Algorithm: The study introduces a fully distributed algorithm that allows a network of mobile robots with onboard sensors to localize themselves and track multiple targets simultaneously.
Robustness: The algorithm is robust to time-varying sensing, communication topologies, and changes in the robots that are directly sensing the targets.
Performance: By considering the mutual influence of localization and target tracking, the algorithm improves performance and maintains consistency in estimates.

## Slide 5: Algorithm for Localization
The DEIF (Distributed Extended Information Filtering) Algorithm for localization is a method used in mobile robot networks for cooperative localization. Here’s a brief explanation:
The algorithm involves initialization, propagation, and update steps where robots use relative measurements, absolute measurements (if available), and information from one-hop neighbors to update their pose estimates. It’s designed to work with generic robot motion and measurement models and is adaptable to time-varying communication topologies

## Slide 6: Steps
Objective: To enable each robot to estimate its own pose using only local information and communication with immediate neighbors12.
Fully Distributed: The algorithm operates without the need for global parameters or multi-hop communication, making it scalable and robust3.
Consistency Guarantee: It ensures that the estimates are consistent, meaning the estimated error covariances realistically represent the actual errors4.
Joint Localization and Target Tracking: The DEIF algorithm accounts for the mutual influence between localization and target tracking to improve performance.

## Slide 7: Algorithm for Target Tracking
The DEIF (Distributed Estimation Information Filter) Algorithm for target tracking is a method used in mobile robot networks to cooperatively estimate the state of a target.
The algorithm allows each robot to contribute to the target state estimation, improving accuracy and robustness in a distributed manner. It’s designed to handle time-varying models and maintain consistency of the estimates.

## Slide 8: Steps
Initialization: Each robot initializes its estimate of the target’s state.
Propagation: Robots propagate their estimates based on their motion models.
Update: Robots update their estimates using local measurements and information from one-hop neighbors.
Fusion: An Inverse Covariance Intersection (ICI) method is used to fuse estimates and avoid double-counting information.

## Slide 9: Conclusion
Distributed Algorithm: The paper introduces a fully distributed algorithm that allows mobile robots to estimate their own poses and track multiple targets using only local information and communication with one-hop neighbors.
Consistency and Stability: The algorithm guarantees consistency and stability under certain conditions, even for linearized time-varying systems, ensuring reliable performance.
Improved Performance: By jointly estimating the robots’ poses and targets’ states, the algorithm achieves better accuracy in the pose estimates of the robots compared to separate estimations.